## Slide 1: Requirement of one stop tool for security tool
Se Team

## Slide 2: Current method

## Slide 3: 3-type security boot and tools used for security boot
3-type security boot
  Authentic boot
  Encrypted boot
  Encrypted XIP
Tools used
  CST tool (command line tool running under Windows command prompt or Linux shell)
  Flash loader tool (tools including blhost, elftosb, sdphost)
  OpenSSL

## Slide 4: 6-step needed to create a security boot
Generate keys and certificates
  create ‘serial.txt’ file for the certificate serial numbers
  create ‘key_pass.txt’ file for pass phrase
  run ‘hab4_pki_tree’ and input for prompted questions
  copy ‘cst’ executable, “crts” folder and “keys” folder to the folder containing ‘elftosb’
Generate SB file for Fuse programming
  run ‘srktool’ to generate SRK_1_2_3_4_xxx files
  add the binary content of SRK_1_2_3_4_ fuse.bin in the enable_hab.bd file with hex string format (3rd party tool or edit manually)
  run ‘elftosb’ to generate ‘enable_hab.sb’ file

## Slide 5: 6-step needed to create a security boot – Cont’d
Generate the signed flashloader
  copy ‘flashloader’ to the folder containing ‘elftosb’ file
  run ‘elftosb.exe -f imx -V -c imx-flexspinor-flashloader-signed.bd -o ivt_flashloader_signed.bin …’
Generate the bootable image
  edit the imx-flexspinor-normal-signed.bd file
  run ‘elftosb.exe -f imx -V -c imx-flexspinor-normal-signed.bd - o ivt_xxx.bin …’ to generate the bootable image

## Slide 6: 6-step needed to create a security boot – Cont’d
Generate the SB file for bootable image
  edit program_flexspinor_image_hyperflash_encrypt.bd file
  run ‘elftosb.exe -f kinetis -V –c program_flexspinor_image_hyperflash_encrypt.bd -o boot_image.sb …’ to generate the SB file used for mfgtool
Program bootable SB files
  copy the boot_image.sb file, ivt_flashloader_signed.bin and enable_hab.sb to “<mfgtool_root_dir>/Profiles/MXRT105X/OS Firmware” folder
  change the “name” under “[List]” to “MXRT105x-SecureBoot” in cfg.ini file in <mfgtool_root_dir> folder
  run ‘MfgTool2.exe’ to program images
If using SW_GP2 key, encrypting user image needs additional step.
  Encrypted XIP using sw_gp2 key isn’t supported by current tool. But more customers need it.

## Slide 7: Disadvantage of Current Method
First 5 steps are done in command line window.
Intermediate files such as serial.txt, key_pass.txt and hex string of SRK hash value are generated by 3rd party tool or manually.
Too many commands with many parameters may cause input error.
Editing BD file is pretty difficult to user. Instructions has no details and are dispersed among several documents.
Setting configuration block with value of specific format for the bootable storage in BD file is also difficult to user.
As a result, current security tools are difficult to use. Many complaints are raised from customers and also from NXP customer support guys: tools are tiring and boring.
Security tool is degrading the reputation of RT.

## Slide 8: ONE stop GUI tool Proposal

## Slide 9: Requirements
Additional function to support image encryption by XIP of SW_GP2 key. (not supported in current tool)
GUI interface, all user operations are done in GUI
Command line tools are invoked under GUI. It’s transparent to user.
Merge the MFGTOOL into GUI as well.
Manual work must be done by GUI tool (For example, SRK hash hex string)
Show the tips while mouse hovers on the Controls.
Support to add more BD-style commands for special case into the BD file if needed ( not sure if it’s really needed)
Current command
lines-based
security tools
GUI interface

## Slide 10: Requirements – Cont’d
Use Tabs for one or more merged steps
Use drop-down list to select boot type (Authentic, or Encrypted, or Encrypted XIP).
Use drop-down list to select different storage type
The available Windows Controls depends on the selected storage and boot type (Authentic, or Encrypted, or Encrypted XIP).
Use a Button for a command with Group Box/Check Box/Radio Box/Edit Windows Controls for parameter or options.
For example (original step 1):
  Use Edit for “serial.txt” and “key_pass.txt”, for example, the default value is given in the GUI, but user can change it.
  Create a “workspace” folder, copy flash loader tools, ‘cst’ executable, “crts” folder and “keys” folder to “workspace”. The following operations will be done in this folder.

## Slide 11: Benefits
A newbie customer without security knowledge can have security boot work quickly with GUI tool.
As for the sophisticated customer, the command line tool and method are still available for them.

## Slide 12: Schedule
Tool should be available asap due to many customers are using security boot tool to protect their code and data for mass production.
More and more complaints on the command line tool are ruining the RT reputation.
Expectation is to have the tool available in 1~2 month.